## Slide 1: Challenge 5: Transportation Economics
Development of an Enhanced User Benefit and Cost Calculator for Ohio
Vince Bernardin, RSG
Chris Beard, BLA
Greg Giaimo, ODOT

## Slide 2: The Big Picture
The Big Questions:
  Bang for your Buck: B/C ratio
  The Bottom Line: Job creation
ODOT’s TRAC project selection process may consider both
  Currently re-evaluating economic measures
  Many alternatives: development/redevelopment potential, ROI, economic distress, etc.
ODOT’s Statewide Planning & Research group has been developing and enhancing tools to quantify these answers for more than a decade (CMSCost, UCOST, EIM, QEIM, etc.)
Tools did not all play well together / with all models – concerns about consistency, and lacked sensitivity to some issues ODOT was interested in: maintenance vs. capital costs, reliability improvements, etc.

## Slide 3: Review of ODOT’s Initial System
Consistency of Demand Model Utility Measures, Path Building Impedances with Economic Assumptions
  Different values of time, differing impedances
  Simple length term in generalized cost not necessarily tracking operating costs, crash costs
Model Stability: Simulation Variation & Assignment Convergence
  Simulation variation limited precision ($100k), but manageable
  Assignment convergence / stability found to be a major issue
Induced Demand, Mode Shift & Travel/Land Use Redistribution
  Ignored in initial system
  Considered Rule of Half vs. Expected Utilities Methods
Comparison of QEIM vs. T-PICS
  Compared economic impacts of 4 projects from QEIM & T-PICS
SEE YOUR FLASH DRIVE FOR THE FULL REPORT (EC-1_REPORT.PDF)!

## Slide 4: QEIM vs. T-PICS
Job creation was similar
  Because driven by construction costs
  Slightly higher net multiplier offset by lower labor productivity
Direct Benefits very different
  QEIM missing effects:
    Consumer Surplus
    Commodity Value of Time
    Travel Time Reliability
    Market Access & Productivity Effects
  Possible bias towards more costly projects over projects with more actual benefits
SEE YOUR FLASH DRIVE FOR A
SPREADSHEET COMPARISON
(Project Testing Summary.xlsx)!
Project | Economic Effect | QEIM | T-Pics
144 Freeway Widening | Employment | 1,362 | 1,385
 | Net Multiplier | 1.80 | 1.56
 | Direct Benefits | $566,907 | $38,659,000
139 New Roadway | Employment | 632 | 640
 | Net Multiplier | 1.75 | 1.66
 | Direct Benefits | $1,349,638 | $17,438,500
117 New Interchange | Employment | 1,136 | 1,435
 | Net Multiplier | 1.75 | 1.56
 | Direct Benefits | $180,282 | $62,632,000
113 Reconstruct Freeway | Employment | 10,112 | 10,425
 | Net Multiplier | 1.73 | 1.66
 | Direct Benefits | $805,471 | $267,088,500

## Slide 5: Recommendations
Improvements to Assignment (presented later in this workshop)
  Improve convergence
  Consistency of generalized cost
Improve Economic Impact Calculator (in early stages of development)
  Enhanced Market Access / New Economic Geography Effects
  Feedback new employment into land use components of statewide model
Improve User Benefit Calculator (presented here)
  Apply Consumer Surplus Theory
  Add Commodity Values of Time
  Add Travel Time Reliability Impacts
  Add Work Zone Impacts
  Incorporate Asset Deterioration / Maintenance Costs

## Slide 6: Improved User Benefit Calculator
UCOST2 Tools
  Integrated with Ohio Statewide TDM
  Compatible with standard Ohio Medium & Small MPO Models
  Analysis also improves Travel Demand Model Results
  Developed as a set of 3 Utilities in CUBE script
    AGEASSET
    PRECOST
    UCOST2

## Slide 7: AGEASSET Utility
Goal: Incorporate Asset Deterioration Impacts & Maintenance Costs in Benefit Cost Analysis
Most Major Projects Include Significant Rehabilitation Components in Their Cost Yet Travel Demand Model Based User Benefit Analysis Only Measures Mobility Benefit
  Example: Replacing a major bridge could be a major project costing hundreds of millions yet if it had the same number of lanes the model based method would indicate zero benefit
Most Major Projects are Hybrids Containing Both Capacity Enhancement and Rehabilitation

## Slide 8: AGEASSET Utility
Tool is Not a Detailed Asset Management Tool, Rather a Planning Level Analysis Based on Averages
Maintenance Strategies Are Simplified as:
  Deferred Maintenance
  Status Quo Maintenance
  Complete rehabilitation/reconstruction
Focused on project area, ignores deterioration elsewhere
Key Outputs Play to Strengths of Travel Demand Model Allowing Mobility Impacts of Deteriorated Assets to be Quantified (Detailed Asset Management Tools Can’t do This)
  Load limits/closures due to deterioration
  Speed reductions due to poor pavement conditions
  ODOT maintenance costs by year

## Slide 9: AGEASSET Utility
Measures of Asset Conditions
  Pavement: International Roughness Index (IRI)
  Structures: Organizational Performance Indicator (OPI)
Key Factors
  Baseline conditions of Pavement & Structures
  Maintenance unit costs per lane mile (e.g., to re-deck structure)
  Average Annual Freeze Index Factor
Utility Operation
  Steps through time
  At each step, calculates deterioration from baseline IRI/OPI based on traffic, climate
  Takes action (or none) based on specified strategy
  Determines any speed reduction, load limits/closures – for assignment
Notes: OPI is ODOT specific measure

## Slide 10: PRECOST Utility
Goal: Incorporate Vehicle Operating Costs and Crash Costs & Delays in Assignment
  Avoid potential inconsistency between costs used to select best route in assignment and costs in economic analysis
Methods: Vehicle Operation & Crash Costs
  HERS Methods for most VOCs
  AASHTO Red Book for most safety
    Considered Highway Safety Manual but left for future
  Published OSU research for work zones
Utility Operation
  Calculate Costs & Delays on Mainlines & at Intersections
    Based on ‘bootstrapped’ traffic levels
    Linearization necessary – economic models not monotonic
  Apply to TDM network for Assignment
Notes: Grades, truck percentage and congestion key factors why operating and crash costs not simply length based

## Slide 11: UCOST2 Utility – Consumer Surplus
Goal: Apply Consumer Surplus Theory & Incorporate Additional Cost Factors
  Consumer Surplus Theory
  Commodity Value of Time
  Travel Time Reliability
  Work Zone Delays & Costs
Consumer Surplus Theory
  Necessary when induced travel / land use are significant
  Applied to total user costs not just travel time
  Used linearization “Rule of Half”
  Expected Utility proved problematic
  Numerical integration possible but time consuming

## Slide 12: UCOST2 Utility – Commodity Value of Time
Commodity Value of Time & Truck Classes
  Considered logistics-based truck classes related to commodity values
  Variation in value of commodity time much less than truck size
  Truck classes based on # of axles & service vs. goods-carrying
    Dovetails better with toll classifications
    Includes wage & benefits + commodity VOT
  Commodity value of travel time reliability may prove more critical
SEE YOUR FLASH DRIVE FOR ADDITIONAL COMPARISONS IN SPREADSHEET (ODOT_Truck_VOT_Summary.xlsx)!
 | PRIVATE | FOR-HIRE |  | 
 |  | LONG-TERM | SHORT-TERM | ON THE SPOT
Average Value ($/ton) | $1.02 | $1.97 | $1.31 | $0.85
Average Value of Time ($/hr/ton) | $0.78 | $0.87 | $0.86 | $0.58
Truck Class | Total Value of Time
Four Tire Service Vehicle | $25.87 / hr
Four Tire Goods Vehicle | $21.14 / hr
SU Truck (2-4 Axle) | $22.42 / hr
MU Truck (5+ Axle) | $34.24 / hr

## Slide 13: UCOST2 – Travel Time Reliability
Travel Time Reliability
  Considered buffer time vs. mean-variance approach
    Buffer time doesn’t require VOR – good or bad?
    Opted for buffer time approach
  ODOT purchased INRIX data statewide on speed, reliaiblity
    Reliability clearly related to average delay
    VDFs do poor job of predicting delay
    Estimated new VDFS, better, but still poor
Chart: TT Variability vs. Delay, Evening
| 0 | 0.05 | 0.1 | 0.15000000000000002 | 0.2 | 0.25 | 0.3 | 0.35 | 0.39999999999999997 | 0.44999999999999996 | 0.49999999999999994 | 0.54999999999999993 | 0.6 | 0.65 | 0.70000000000000007 | 0.75000000000000011 | 0.80000000000000016 | 0.8500000000000002 | 0.90000000000000024 | 0.95000000000000029 | 1.0000000000000002
Urban Street | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.075 | 0.16 | 0.245 | 0.33 | 0.415 | 0.5 | 0.585 | 0.67 | 0.755 | 0.84 | 0.925 | 1.01
Urban Freeway | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.048 | 0.286 | 0.524 | 0.762 | 1
Rural Divided | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.1065 | 0.237 | 0.3675 | 0.498 | 0.6285 | 0.759 | 0.8895 | 1.02
Rural Other | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.045 | 0.12 | 0.195 | 0.27 | 0.345 | 0.42 | 0.495 | 0.57 | 0.645 | 0.72 | 0.795 | 0.87 | 0.945 | 1.02
Source: Sam Granato, ODOT
Chart: VDFs estimated from INRIX
| 0 | 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004
 | 1 | 0.99999 | 0.99976 | 0.99879 | 0.99617 | 0.99071 | 0.98093 | 0.96524 | 0.94212 | 0.9104 | 0.86957 | 0.81993 | 0.76275 | 0.70008 | 0.63442 | 0.56838 | 0.50428 | 0.44389 | 0.3884 | 0.33843 | 0.29412
 | 1 | 0.9983 | 0.99323 | 0.98489 | 0.97344 | 0.95912 | 0.94217 | 0.9229 | 0.90162 | 0.87865 | 0.85434 | 0.82898 | 0.80288 | 0.77631 | 0.74952 | 0.72274 | 0.69615 | 0.66991 | 0.64416 | 0.619 | 0.59453
 | 1 | 0.99997 | 0.99956 | 0.9977 | 0.99266 | 0.98205 | 0.96312 | 0.93321 | 0.89045 | 0.83445 | 0.76675 | 0.6907 | 0.61073 | 0.53137 | 0.45636 | 0.3882 | 0.32811 | 0.27634 | 0.23244 | 0.19561 | 0.16493
 | 1 | 0.99824 | 0.99298 | 0.98434 | 0.97249 | 0.95767 | 0.94016 | 0.92027 | 0.89835 | 0.87473 | 0.84976 | 0.82377 | 0.79707 | 0.76995 | 0.74265 | 0.71541 | 0.68842 | 0.66183 | 0.6358 | 0.61041 | 0.58575
 | 1 | 0.99838 | 0.99354 | 0.98558 | 0.97464 | 0.96094 | 0.9447 | 0.92621 | 0.90574 | 0.88362 | 0.86014 | 0.8356 | 0.81028 | 0.78444 | 0.75832 | 0.73214 | 0.70609 | 0.68031 | 0.65495 | 0.63013 | 0.60591
 | 1 | 0.99815 | 0.99264 | 0.98359 | 0.97119 | 0.9557 | 0.93743 | 0.91672 | 0.89393 | 0.86943 | 0.8436 | 0.81677 | 0.78928 | 0.76143 | 0.73347 | 0.70564 | 0.67814 | 0.65112 | 0.62473 | 0.59906 | 0.57418
 | 1 | 0.99778 | 0.99119 | 0.98039 | 0.96567 | 0.94737 | 0.92593 | 0.90181 | 0.8755 | 0.84747 | 0.8182 | 0.78811 | 0.75759 | 0.727 | 0.69662 | 0.66669 | 0.63742 | 0.60895 | 0.58142 | 0.5549 | 0.52944
 | 1 | 0.99804 | 0.99219 | 0.9826 | 0.96949 | 0.95313 | 0.93387 | 0.91209 | 0.88819 | 0.86257 | 0.83563 | 0.80775 | 0.77927 | 0.75051 | 0.72174 | 0.6932 | 0.66509 | 0.63757 | 0.61076 | 0.58477 | 0.55966
Source: RSG

## Slide 14: UCOST2 Utility – Work Zone Delay & Cost
Work Zone Delays & Costs
  Implemented methods from research at OSU published in JTE
  Work zone delay, crashes and additional vehicle operating costs as a function of traffic, length of closure
Source: Jiang, X. and H. Adeli (2003) “Freeway Work Zone Traffic Delay and Cost Optimization Model”, JTE