## Slide 1: Modeling University Student Trips Separately from the General Population
In a Regional Travel Demand Model
Presented to
15th TRB National Transportation Planning Application Conference
May 21, 2015
Atlantic City, New Jersey
Presented by
Chao Wang, Cambridge Systematics, Inc. (Email: cwang@camsys.com)
Joseph Huegy, Institute for Transportation Research and Education

## Slide 2: Background
More and more university student surveys are conducted
  4 universities in Virginia (2009, 2010)
  Arizona State University (2012)
  8 colleges/universities in Utah (2012)
  2 universities in Texas (2013)
  6 universities in North Carolina (2013, 2014)
  Compared to the general population, university students have
  Higher trip rate
  Shorter trip distance
  Different time of day distribution
  Higher shares of non-motorized and transit trips

## Slide 3: Methods
Current practices
  No special treatments
  Introduce special generators
  Model Home Based University trips
Proposed method
  Model university students separately from the general population
    Different trip purposes
    Different market segmentations
    Different models

## Slide 4: Triangle Regional Travel Demand Model (TRM)
TRM is a trip based four-step model
1.6 million population
Four major universities in the region (about 80K students)
  North Carolina State University (NCSU)
  University of North Carolina at Chapel Hill (UNC)
  Duke University (DUKE)
  North Carolina Central University (NCCU)

## Slide 5: Is it worth the hassle to model university students separately?
Chart: Population
| Students at four universities | Other population
 | 79621 | 1559034
Chart: Transit Ridership
| Students at four universities | Other population
 | 39126 | 44121
Notes: “All Strata” and “Strata 1 and 2” are from HHS. “Off-Campus Student” and “On-Campus Student” are from NCSU Student Survey. The numbers in parenthesis are from HHS.

## Slide 6: Challenges
How to separate off-campus students from the general population
  Collect student home addresses from universities
  Population synthesizer
  Off-campus student residence location model
    Determine the total number of HBU trips made by off-campus students
    Develop a discrete choice model to locate the home ends
    Calculate the zonal number of off-campus students, based on the HBU trip rate as a function of the distance to campus

## Slide 7: Validation - distribution of distance from home to campus
Chart: 
| Less than 2 miles | 2-5 miles | 6-10 miles | 11-20 miles | Over 20 miles
2011 UNC Commuting Survey | 0.368 | 0.293 | 0.19 | 0.033 | 0.116
2009 UNC Commuting Survey | 0.401 | 0.263 | 0.168 | 0.04 | 0.128
2007 UNC Commuting Survey | 0.27 | 0.389 | 0.124 | 0.104 | 0.112
Residence Location Model | 0.2863 | 0.41801 | 0.1356 | 0.12417 | 0.035912

## Slide 8: Summary
The impact of university student trips on a travel demand model might be big enough to require a separate model from the general population.
Off-campus students are usually treated as household population in the socio-economic data. They need to be separated from the general population carefully.