## Slide 1
New Experience Expanding Truck GPS-Based Origin-Destination Data in Tennessee
May 20, 2015
Erich Rentz, RSG
Vince Bernardin, PhD, RSG
Steven Trevino, RSG
Jeff Short, ATRI
Robert Rock, TDOT
15th TRB National Transportation Planning Applications Conference

## Slide 2
ATRI Board of Directors

## Slide 3
Ongoing Truck GPS data research beginning in 2001
Comprehensive North American Truck GPS dataset
“Big Data”
  Real time data feeds/ significant hardware and software
  Currently near 100 million data points per day
  Will approach 1 billion points per week later this year
Fully deployed applications
  Performance measurement/management
  Freight flow and truck trip modeling
Key research areas
  Economic competitiveness and supply chains
  Truck volume/intensity/national travel patterns
  Weather, parking, emergency events
ATRI Truck GPS Dataset

## Slide 4: ATRI Truck GPS Dataset – One Day

## Slide 5: ATRI Truck GPS Dataset

## Slide 6: ATRI Truck GPS Dataset

## Slide 7: ATRI Truck GPS Dataset

## Slide 8: ATRI Truck GPS Dataset

## Slide 9: ATRI Truck GPS Dataset

## Slide 11: ATRI Truck GPS Dataset

## Slide 12: ATRI Truck GPS Dataset

## Slide 13: ATRI Truck GPS Dataset

## Slide 14: ATRI Truck GPS Dataset

## Slide 15: ATRI Truck GPS Dataset

## Slide 16: ATRI Truck GPS Dataset

## Slide 17: Modeling Applications
PRIOR USAGE OF ATRI TRUCK GPS DATA
  2012 Indiana Statewide Travel Demand Model Update
    RMSE: 69.3% to 60.6%
    MAPE: 74% to 42%

## Slide 18: Iowa Dataset
DETAILS OF ATRI TRUCK GPS DATA WITHIN IOWA
  Four 2-week samples from each quarter of 2012
  Over 135,000 individual trucks
Notes: This also includes two weeks of 2013
  Truck positions paired into “pings”
  Data Privacy – Anonymous IDs, GPS coordinates to TAZs
  Ping Dataset : IDs, timestamp, distance, start/end TAZs

## Slide 19: Data Processing
ATRI PING DATASET MUST BE PROCESSED TO TRIP O-D PAIRS
  Identifying movement for all records
  Determine trip O-Ds, travel time, VMT

## Slide 20: Data Processing

## Slide 21: Data Cleaning
METHODS INTRODUCED TO IMPROVE PROCESSING
  Over 50 million movement records from 135,000 trucks
  Data Filtering:
    GPS jumps – urban canyons, mountains, spatial joins, etc.
    Missing data – spatial joins
    Study period edges – trips in progress
    Duration & OD mismatch – missed stops, GPS jumps
  Applied conservative filtering methods in Iowa
  Working on more intelligent filters

## Slide 22: GPS Blips

## Slide 23: Circuity

## Slide 24: Start & End Time

## Slide 25: Processing Results & Scaling
DATA CAPTURES ROUGHLY 10% OF TRUCKS OVER 56 DAYS
  Processed data contains:
    2.8 million truck trips over 56 days
    60,656,488 VMT within Iowa
    1,083,152 Daily Average VMT
    10,731,507 Iowa DOT estimated 2012 daily truck VMT
    Sample rate of 10.1%
  Factored raw data by 0.1769 to represent daily preliminary seed OD table

## Slide 26: Weighting & Expansion
GOAL FOR IOWA TO MOVE BEYOND SIMPLE SCALING
  Initial statewide truck modeling application of ATRI data in Indiana stopped with scaling
  ATRI data is not a random sample – suspected some biases
  Anecdotal evidence for geographic/regional & trip-length (short-haul) biases
  Developed a weighting scheme to address these sample biases using ODME

## Slide 27: Geography
NO EVIDENCE OF SYSTEMATIC GEOGRAPHIC BIAS
  Geographic differences of sample coverage in Iowa / Halo area

## Slide 28: Trip Length – Short Haul / Long Haul
BIAS TOWARDS LONG HAUL
  Confirmed suspected bias of long-haul over short-haul truck trips
  Bias was not as strong as some may have supposed
Chart: Trip Length (min)

## Slide 29: Weighting Scheme
WEIGHTING SCHEME BASED ON TRIP LENGTH
Chart: Trip Length (min)
| 10 | 20 | 30 | 40 | 60 | 100 | 140 | 180 | 220 | 260 | 300 | 340 | 420 | 500 | 600 | 1000
Weight | 2.5283 | 1.7784 | 1.5226 | 1.2916 | 1.0634 | 0.90447 | 0.87601 | 0.81781 | 0.78462 | 0.78624 | 0.77596 | 0.75964 | 0.7314 | 0.73966 | 0.71832 | 0.79626

## Slide 30: Truck Assignment Tests
TRUCK ASSIGNMENTS MADE FOR TESTING PURPOSES ONLY
  ATRI data used as one component of truck model
  Assignment used to assess count consistency, weighting effectiveness, goodness-of-fit bounds
  Previous model used ODME to achieved 81% RMSE for trucks
Assignment Type | RMSE
Scaled Data | 116%
Weighted Data | 92%
ODME on Data | 58%
Notes: 63,044 counts

## Slide 31: Tennessee
ATRI DATA SAMPLE FOR TENNESSEE
  Similar four 2-week samples over 2013 quarters.
  235,000 unique trucks.
  138 million records processed to 5.8 million trips.
  84,147,030 truck VMT within TN.
  Sample rate of 6.5% vs. total trucks
  Sample rate of 10.7% vs. multi-unit trucks

## Slide 32: Conclusions
  ATRI’s truck GPS data provides a rich and growing source of information on truck travel patterns
  It is a large sample – but still a sample
  Failure to properly expand it could lead to under-representation of short-haul movements and faulty analysis or false conclusions
  Weighting offers both:
    an understanding of ODME
      Confirmation and measurement of long-haul bias
      Mixed findings on geographic sample rates
  and an alternative to ODME
      No ODME uncertainty or individual OD adjustments
  Better Data + Better Analysis =
  Better Models + Better Planning