## Slide 1: Corridor-Focused Transit Survey Data Collection and Application in South Florida
15th TRB National Transportation Planning Applications Conference, Atlantic City NJ
May 20, 2015
Presented by
Ashutosh Kumar, AECOM

## Slide 2: The Problem
Multi-modal corridor studies typically suffer from lack of corridor-level transit data that is
  Up-to-date,
  Sufficiently detailed, or
  Of sufficient quality for corridor analysis
Pre-planning for these types of studies is generally limited to the collection of readily-available, system-/region-wide travel data/model

## Slide 3: The Consequence
Multi-modal corridor studies that use their resources inefficiently and suffer from high schedule-delay risk
  Data collection: limited windows of opportunity (Jan-Apr/Sep-Nov), data processing time
  Technical tools: regional models and other route planning tools (such as TBEST in Florida) are not sufficiently prepared for corridor analysis or may not be most appropriate for some corridors
  Tight schedule because downstream funds are programmed in next FY (1-2 month delay  1 fiscal year delay)

## Slide 4: Objectives
Identify issues in advance to inform project scope development
Move data collection and model development outside of the project
  Better control of costs/delivery of the data and models
  Reduce study distractions from the data/model work
  Keep focus on the study analysis and consensus efforts
Faster delivery of projects to NEPA/design phases

## Slide 5: FDOT District 4 Program
District 4 covers Ft. Lauderdale and West Palm Beach metro areas in South Florida; includes 5 counties (Broward, Palm Beach, Martin, St. Lucie and Indian River)
Program initiated in FY 2012
Six corridors covered so far in Broward County covering 45% of the system-wide boardings
The program is in second iteration right now
  Survey methodology, processing and application updated with lessons learned and industry research after each survey

## Slide 6: Methodology
Collect and analyze readily available corridor data
Conduct state-of-the-art corridor-focused field travel surveys
Utilize the data to
  Develop preliminary case for the project based on the readily available and collected data
  Develop efficient corridor data-driven simplified ridership model
  Develop other data driven route planning applications to support transit agencies plans

## Slide 7: Readily Available Data Collection and Analysis
Demographic data: latest SERPM model, Census/ACS
D2D trip flow data: ACS, CTPP 2000, SERPM
Roadway and Traffic Characteristics: Florida Traffic Information data, HERE/INRIX data
Transit data: Public time table, system-wide on-board, existing APC and farebox data
Etc..

## Slide 8: Corridor-Specific Transit Data Collection
Two surveys conducted
  Boarding-to-alighting (B2A) survey
    Card distributed to rider, and returned to surveyor when rider alights
    Captures boarding and alighting stops for each rider
    40-55% sample rate (4-5x standard transit O/D survey)
  Simplified main survey, asking questions oriented to route:
    Origin and destination, Up- and down-stream transfers, Trip purpose, Others as necessary
    ~20% sample rates (2x standard transit O/D survey) – rates determined by period, segment-to-segment flows
Platform/intersection surveys as necessary
  Retirement community residents versus workers
  Transfer patterns at intersections
  Mall terminal patterns

## Slide 9: Field Travel Surveys – “What’s Uncommon Here”
On-board survey with portable smart devices (first transit application in South Florida area):
  Real-time update and accumulation of survey data
  Real-time geo-coding of the riders’ origin/destination addresses plus boarding/alighting stops
  Real-time in-field quality control measures with built-in algorithm
  State-of-the art sampling plan based on segment-to-segment flows rather than at route level
Local survey crew staff – most of them sufficiently trained and experienced over multiple surveys

## Slide 10: A Comparison of Approaches: An Actual Example (Route 18)
 | Traditional (Regional transit survey) | With Pre-Planning & Data Collection (Corridor-specific transit survey) | Notes
Riders making at least one transfer | 49% | 67% | More riders transferring than previously thought; different routes and magnitudes
Top 4 transfer routes | 22, 72, 34, 36 | 72, 36, 7, 34 | 
Percentage of work trips | 43% | 49% | Relatively similar
Average trip length (overall) | 8.33 miles | 7.18 miles | Previous estimates over-stated trip lengths (long-trip response bias)
Average trip length (on bus) | 6.54 miles | 4.93 miles | 
Sub-route travel movements | Insufficient information | Detail information; created trip table | Now have better data to inform route planning

## Slide 11: Application of the Data 1. standard tables and Maps from the survey 2. data-driven route planning application 3. data-driven simplified model 4. preliminary case for the project document

## Slide 12: Data Application – Transit Rider Desire Line Map
“Standard” set of analyses to understand the market…
Source: Connetics Transportation Group

## Slide 13: Data Application – Route Planning Application Interface
Simple Application for understanding route travel patterns.

## Slide 14: Route Planning Application – Trips by Purpose Example

## Slide 15: Route Planning Application – Segment to Segment Flows Example
Dynamically displays segment-to-segment flow information using D3 (Data Drive Documents) technology

## Slide 16: Data Application – Data-Driven Ridership Model
Ingredients
  Route-specific survey data, supplemented with system-wide survey
  Auto skims, person trip tables, and transit networks from regional travel model
  Incremental logit mode choice model (pivot-point)
    TCRP Report 118: BRT Practitioner’s Guide
  Cube Voyager platform
Development time/cost: 2 months and ~$30,000 (for high ridership routes)
15% of regional model running time (6x faster)

## Slide 17: Preliminary Case for the Project Documentation
Initial draft completed by pre-planning team using the readily-available and the collected data (3-4 pages)
  Project identification and setting
  Current (base year) conditions
  Near-term and horizon-year changes
  Enumeration of corridor transportation problems
Remaining sections to be completed by project team during corridor study (3-4 pages)
  Purpose of the Project
  Merits of the Low-Cost and Locally-Preferred Alternatives
  Uncertainties: Ridership
  Summary

## Slide 18: Reactions / Summary
Highly favorable reactions from the local transit agency and FDOT staff
Pre-planning & data collection efforts provide many benefits to transit planners
  Improved understanding of corridor
  Focused use of resources
  Reduced schedule delay in corridor studies
  Adopted to better assess unique corridor travel market

## Slide 19: Acknowledgments
Scott Seeburger and Shi-Chiang Li, FDOT
David Schmitt and Hongbo Chi, AECOM
FTA