## Slide 1: Comprehensive Validation of Activity-Based Models
Experiences from Houston-Galveston Area Council’s Activity-Based Model Development
TRB Applications Conference
May 21, 2015
Martin Milkovits
Arun Kuppam
David Kurth
Thomas Rossi

## Slide 2: H-GAC ABM Structure
Tour-Level Choices
Long-Term Choices
Stop/Trip-Level Choices
All Tour Stop Generation and Mode Choice
Tour Generation
Mandatory Tour Destination and Time of Day
Auto Ownership, Work Location, School Location
Daily Activity Pattern (Including Work/School Travel)
Fully Joint Travel
Stop (Trip)-Level Destination, Time of Day, and Mode Choice
Individual Nonmandatory Travel
School Escorting Model
Joint Tour Destination and Time of Day
Individual Nonmandatory Tour Destination and Time of Day
Notes: Point out logsums from Tour Mode Choice
School Escort / Fully Joint intra-household coordination

## Slide 3: Validation Approach
  Identify key areas of future analysis
  Compile validation data
  Assure correct model operation
Prevalidation
  Population synthesis validation
  Single-pass validation (TourCast)
  Full-feedback validation
  Sensitivity test
  Elasticity test
  Backcast test
Validation Tests
Notes: First bullet – true of any model (Trip or ABM, but ABM sensitivities are more complex)
Second – ABMs are developed to provide specific insights for the client, these are examples that H-GAC is particularly interested in
Future analysis areas:
  Reversible HOT lanes
  Environmental Justice / Title 6 analysis
  Sustainable livable centers

## Slide 4: Sensitivity Tests
Straight-forward to setup
  Synthesized population
  Land use data
  Networks
  Model parameters
  Fix random seed
Wide array of potential scenarios
  Time dependent
  Demographic profile

## Slide 5: Example scenarios
Scenario | Expected Result
Increase auto operating costs | Mode shift, reduced tour length, reduce activities
Reduced transit fare | Mode shift
Parking cost increase | Mode shift, tour destination change
Increase toll by time of day | Mode shift, time shift, tour destination change
New employment center | Mode shift, tour destination change
Aging population | Fewer work tours, mode shift

## Slide 6: Examine variations across components
Activity Pattern
Tour Generation
Destinations
Time of Day
Trip-Chaining
Mode Choice
Assignment
Chart: 
| work | school | uni | non-mand
Arrival | -0.0032598 | -0.00044295 | -0.0046237 | -0.01194
Departure | -0.0031415 | -0.0012378 | -0.0059469 | -0.014
Chart: 
| < $20K | $20-40K | $40-70K | $70-100K | >$100K
Arrival | -0.0030709 | -0.0034384 | -0.0026139 | -0.0024865 | -0.0022588
Departure | -0.0029703 | -0.0030482 | -0.0021149 | -0.0026408 | -0.0018831
Change in Tours in Peak Period with Peak Period Toll Increase

## Slide 7: Lessons Learned
Comprehensive validation reports support sensitivity tests and other model analyses
Sensitivity tests key to evaluate model capabilities and assure correct operation
Useful training opportunity

## Slide 8: It takes a village…
Chris van Slyke, Chi-Ping Lam, Sharon Ju, Heng Wang, David Gao, Michael Onuogu
H-GAC
Vincent Sanders
Houston Metro
Andy Mullins
Texas Transportation Institute
Pat Coleman, Srikanth Neelisetty, Nagaruju Kashayi
AECOM
Vijay Mahal
HDR