## Slide 1: Utilizing Advanced Practice Methods to Improve Travel Model Resolution and Address Sustainability
Bhupendra Patel, Ph.D., Senior Transportation Modeler
Association of Monterey Bay Area Government (AMBAG)
Paul Ricotta, Principal Engineer
Caliper Corporation

## Slide 2: Monterey Bay Area
    Central Coast of California
    Metropolitan Planning Organization (MPO)
    Covering 3 Counties, 18 Cities
    735,708 Population in 2010
    66% Population live in cities
    885,000 Population by 2035
    Major Employment: Agriculture, Service, and Government

## Slide 3: Modeling Challenges
Influence of SF Bay Area
  Heavy commuter trips, telecommuting, flex schedule
Job-Housing Imbalance
  Coastal area vs. inland rural county area
Agriculture activities
  Farm workers are transient/ seasonal
Aging population (65 +)
  Attracts service trips, retirement homes
Longer trip length
Tourists attractions
  Weekend, seasonal variation and special events

## Slide 4: AMBAG RTDM Updates
AMBAG Regional Travel Demand Model (RTDM) recently underwent a significant overhaul
Completely re-estimated using local survey data
Implements Short and Medium Term Improvements recommended by 2011 TMIP Peer Review panel
Considers Long-term improvement strategy
A step closer to an Activity Based Model (ABM)
Upgrade travel model in response to;
    Better measure transportation and land use relations
    Integrate GHG modeling to address SB375 requirements

## Slide 5: Hybrid Approach
Implements advanced practice techniques such as population synthesis to drive a disaggregate trip generation
Destination choice modeling to aid in better alignment of housing to job location
Provide increased model sensitivity to land use changes and 4D measures (Density, Diversity, Design, and Destinations)
  Capture individual-based travel behavior
  Streamline reporting to increase productivity and efficiency

## Slide 6: Trip Generation
Disaggregated trip generation approach
  Population Synthesis
    Sophisticated nested population synthesis routine
    Anchoring the socio-economic component
  Productions calculated on a person basis
  Population derived from a synthetic population
  Match totals of HH’s by:
    Size at Block level
    Income Category, Workers, Auto Ownership at Block Group
    Persons over 65 years of age and under 18 years of age residing in household at Block Group
  Estimating future years synthetic population is a challenge

## Slide 7: Trip Distribution
Fully estimated destination choice framework
  Assists in better aligning workers with their job locations
Deployed destination choice model
  Other home-based trip purposes to better align non-work travel choices
Includes shadow pricing to match attraction totals
Utilizes a tract-based approach for choosing destination
“D” measures incorporated for several purposes wherever found to be significant in model formulation.
Continued use of Gravity for purposes thought to be more proximity-based (e.g., NHBW/NHBO)

## Slide 8: Mode Choice Structure

## Slide 9: Mode Split
Significant upgrade to nested logit structure
  Utilizing a completely estimated formulation
Utilizes “D” measures wherever they were found to be significant
Allowing sensitivity to changes in land use policy resulting in increased accessibility to destinations via transit or non-motorized modes.
Exceptional match on observed mode shares (HH Survey)

## Slide 10: Highway Assignment : Daily Flows
Chart: Count (vpd)