## Slide 1: Improving the Treatment of Priced Roadways in Mode Choice
15th TRB National Transportation Planning Applications Conference
May 19, 2015
Thomas F. Rossi Birat Pandey, Baltimore Metropolitan Council Jason Lemp, Cambridge Systematics, Inc. Martin Milkovits, Cambridge Systematics, Inc.

## Slide 3: How Should Road Pricing Be Treated within the Modeling Process?
A Jabba that is a Hutt topic
Is it a mode choice? Is it a route choice?
What are the advantages of each way of modeling priced roadways?
Has there been research into which way is better?
Does it matter whether the underlying model is activity based?

## Slide 4: Important Concepts
Models oversimplify decision making by separating and sequentializing choices
Value of time
Aggregation

## Slide 5: The Concept of Value of Time
In aggregate applications, a single value of time used per segment during highway assignment
  Auto vs. truck
  Income level
  Value of time level (how to define)
Value of time implied by mode choice model parameters
  Often lower than those assumed in assignment
What affects value of time?
  Trip purpose
  Commercial vs. personal travel
  Income level
  Mode of travel?
  Personal characteristics

## Slide 6: Aggregation in Travel Models
All models have some aggregation – most have quite a bit…
  Geographic (zones)
  Demographic/land use segmentation (income levels, employment types, etc.)
  Time periods
Many ways to reduce aggregation error
  Smaller zones
  Introducing or increasing segmentation
  Simulating individuals (ABM)
  Increasing the number of choice alternatives
Aggregation cannot be completely eliminated in a practical modeling setting.

## Slide 7: Modeling Road Pricing on an Ideal Planet
Each traveler would be simulated individually
  Individualized values of time
  Individualized path choices
OK, who wants to create different skims for every traveler in the region?
Not me

## Slide 8: So We Have to Use Segmentation in Analyzing Priced Roads
We definitely want to segment in highway assignment
  Based on value of time to the extent possible
  Number of segments is a tradeoff between desire for disaggregation vs. practical considerations (e.g., run time)
Segment in mode choice???
  Some models have “toll vs. free” auto mode alternatives
  Is choice of a priced roadway a mode or route choice?

## Slide 9: Toll Alternatives in Mode Choice
“Free” alternatives
  Skimming chooses best path that uses only free routes
  Value of time irrelevant (cost not considered)
  Choosers are excluded from choosing any highway paths using toll roads in highway assignment
“Toll” alternatives
  Skimming chooses best path that uses any route
    But assumes a single value of time per segment (maybe only one)
    Path might or might not include toll roads
    Only one toll path considered
  Choosers may take highway paths using toll roads in highway assignment
    But they don’t have to

## Slide 10: Here’s an (Overly Simple) Example
A
B
C
D
TimeA = 9 CostA = $1.00
TimeB = 18 CostB = zero
TimeC = 5 CostC = $0.60
TimeD = 13 CostD = zero
TimeAC = 14 CostAC = $1.60
TimeAD = 22 CostAD = $1.00
TimeBC = 23 CostBC = $0.60
TimeBD = 31 CostBD = zero
Origin
Destination

## Slide 11: Example Path Choices by Value of Time
Value of Time Range ($/hr) | Path Choice
$0.00-$4.50 | BD
$4.50-$6.67 | BC
Over $6.67 | AC
Assumed VOT | “Toll” Choice | “Free” Choice
$5.00 | BC | BD
$10.00 | AC | BD

## Slide 12: Therefore…
Having “toll” vs. “free” choices in mode choice provides two segments instead of one
Path choices are related to value of time
But there may be many more than two options in reality
And remember…
In static equilibrium assignment, not all of the “toll” users will use a “toll” path

## Slide 13: Can We Do Better?
More segmentation
  Segment by trip/tour purpose in assignment
  Segment by income level in assignment
But…
  We would still have only two paths per segment
  And value of time is correlated with but not only dependent on income level
And…
  Our mode choice model would get more complex
  We would have another set of skims plus another vehicle class in assignment per segment)

## Slide 14: Extending and Improving the Concept
Define segments by value of time level for mode choice
Use a single set of skims per VOT segment
Do not require “free” paths for lowest VOT segment
Use same segments in creating trip tables for assignment

## Slide 15: Proposed Approach for Baltimore Activity Based Model (InSITE)
Estimate VOT distributions
Define a set of VOT ranges
Obtain skims for each VOT level
Simulate specific values of time for each person
When applying the mode choice (and other) models for each person, use the skims pertaining to that person's VOT
Segment highway assignment by VOT level

## Slide 16: Proposed Approach for a Trip Based Model
Estimate VOT distributions
Define a set of VOT ranges
Obtain skims for each VOT level
Applying the mode choice model separately for each segment, using the skims pertaining to that segment's VOT
Segment highway assignment by VOT level

## Slide 17: Benefits of Approach
Segmentation not used to create separate alternatives in mode choice
  Rather, mode choice applied separately for travelers in each segment (so fewer mode choice alternatives)
  Segments are retained for the highway assignment.
Value of time segmentation not expected to be as limited
  More than two segments may be created
No guarantee that a “free” path will be used
  Likelihood of a free path would be higher lowest VOT segment

## Slide 18: Important to Remember…
Not all aggregation is eliminated in this method
VOT ranges are aggregate
Highway assignment is still an aggregate process
But…
A future enhancement could use DTA (Maryland SHA SHRP C10 implementation project)

## Slide 19: Thank You! MAY THE FORCE BE WITH YOU!