## Slide 1: Forecasting the Operational Impacts of Bus Rapid Transit Projects
A Survey of Current Practices
in North America
May 19, 2015

## Slide 2: Bus service enhancement in San Francisco
Notes: Here’s Van Ness Ave as it passes SF City Hall. Van Ness Ave is a key arterial and transit corridor in San Francisco. This will also be the location of San Francisco’s first bus rapid transit corridor.

## Slide 3: Bus service enhancement in San Francisco
  Future bus rapid transit corridors
    Van Ness Ave
    Geary Blvd
    Geneva Ave
    16th St
  Muni Forward
Notes: But Van Ness is not the only BRT corridor under development. Three others are in some stage of planning.
The first two projects are far enough along to say that they will include dedicated lanes, low floor buses, all-door boarding, quality stations, frequent service, signal priority, real time bus arrival info. In both cases bus lanes were assumed, but alternatives analysis considered alignments with side lane (in current right-most lane adjacent to on-street parking) bus lanes and center-running bus lanes. In general, side-running lanes would be cheaper to implement, but center-running lanes are perceived to have better travel time benefits. Given these trade-offs a key concern in project analysis has been to understand relative travel time savings of different possible design elements.

## Slide 4: BRT project planning Considerations
  Considerations
    Cost
    Ridership
    Stakeholders
    Traffic and parking impacts
    Environmental
    Fleet management
    Economic development
    Travel time
    Reliability
Notes: In the real world planning process, a broad variety issues are considered in project alternative definition. But travel time and reliability stand out in importance. 1. they directly influence other measures of success such as ridership, and 2. they form the basis of the benefits on which other trade-offs are made. They are also difficult to understand. Whereas we know a fleet with mixed vehicle types is harder to manage than single vehicle fleet and that a business that is concerned about parking will prefer more parking.

## Slide 5: BRT project planning Purpose and needs
      “Existing transit service” … “is unreliable, slow, and crowded, and is in need of improvement in order to promote high ridership and competitiveness with other travel modes.”
Speed and reliability are key objectives
Notes: This is an excerpt from one of our official purpose and need statements for a BRT corridor in San Francisco. The speed and reliability is of transit service is a key concern in addition to others.

## Slide 6: San Francisco CTA BRT modeling framework
ABM w/ Static
Assignment (CHAMP)
Analytical Traffic
Assessment (Synchro)
Microsimulation
(VISSIM)
Dynamic Assignment
Model (Dynameq)
Auto Demand in Subarea
Intersection
Volumes
Roadway Performance
Roadway Performance
Transit Performance
Auto
Demand
Land
Use
Transportation
System
Transit &
Non Motorized
Demand
Bus travel time
Bus travel time
Bus travel time
Ridership forecasts
Notes: This is the approach we have used in planning and environmental review for our more advanced BRT projects. Used for traffic impacts, ridership projections, and to develop estimates of bus run times and reliability changes. It is a fairly intensive process. Requires a lot of input data, a lot of model validation and calibration. And in practice required a lot of intermediate adjustments, post-processing, and alternate tool development in order to work effectively.
Note, discuss where transit operations estimates come from.

## Slide 7: Perceived modeling tradeoffs
 | Simulation | Alternate Approaches
Pros | Analysis detail Corridor specifics Interactive results | Simplicity Empirically derived
Cons | Higher cost More data needs Longer timeline Black box parameter creep Not everything that matters included | Hard to estimate interactive effects Applicability and range uncertainty
Notes: Perceived trade-offs between complicated modeling structure and sketch planning methods, e.g. spreadsheet to calculate TT savings based on BRT features, etc.
Cons of simulation
- Parameterization decisions lead to different policy recommendations
Models don’t necessarily capture TT reliability, NMT behavior, signal priority in practice, vehicle violations, etc.
Cons of Sketch methods
How applic for local context? (compare w/ ITE trip gen, urban planners long frustrated by ITE trip gen rates derived from suburban examples being used to set urban policy)
5 to 30s TT savings per block! When is it 5, when is it 30?

## Slide 8: BRT modeling investigation Reconsidering SFCTA methodology
  I’m going to:
    Inventory US BRT systems
    Review published guidance on BRT system planning
    Research planning and forecasting of operations benefits
    Interview planners at relevant agencies about transit operations forecasting
    Assess effectiveness of “simpler” approaches
Alex Grant
Notes: Here is the problem statement. Is it worth it for us to go through our extensive process. Could we achieve similarly effective forecasts of TT savings with quicker methods?
Here is our approach for this study

## Slide 9: Bus rapid transit and bus priority Systems in the United States
Source: batchgeo.com
Notes: Close to 20 implemented projects that could be considered BRT or BRT-light. Many more in planning, especially in regions that have already implemented systems.

## Slide 10: Bus rapid transit and bus priority System features

## Slide 11: Guidance Organizations
  Transit Cooperative Research Program (TCRP)
  Federal Transit Administration (FTA)
  United States Department of Transportation (USDOT)
  Center for Urban Transportation Research (CUTR)
  National Bus Rapid Transit Institute (NBRTI)
  EMBARQ
  The Institute for Transportation and Development Policy (ITDP)

## Slide 12: Guidance Documents
  TCRP 90 V.2 (2003)
      This report covers the main components of BRT and outlines the desirable conditions for implementation of a BRT system.
  TCRP 118 (2007)
      A practitioner’s guide that serves as a holistic approach to planning, designing and implementing a Bus Rapid Transit system.
  FTA/USDOT: Characteristics of BRT for Decision Making (2009)
      Contains basic information and data that supports the development and evaluation of BRT systems.
  ITDP: Bus Rapid Transit Planning Guide (2007)
      Comprehensive guide for planning, designing and implementing a BRT system.
  EMBARQ: Social, Environmental and Economic Impacts of BRT Systems (2013)
      Synthesizes information regarding costs and impacts and aims to contribute new evidence from case studies.
Notes: Here is our approach for this study

## Slide 13: Guidance Example – TCRP 118 on running ways
Notes: Here is our approach for this study

## Slide 14: BRT modeling elsewhere What have others done?
  Traffic operational
    Regional travel demand model
    Synchro, VISSIM
  Ridership
    Regional travel demand model, STOPS
    Spreadsheet-based calculations, elasticities
  Transit operational
    Detailed analysis of existing travel time
    Spreadsheet-based calculations (simulation highly uncommon)
    Avoided publicly announced expectation
    Used experience from previous corridors

## Slide 15: U.S. BRT systems Forecasted run time performance
Chart: Preexisting Run Time
| 3.3333333333333333E-2 | 1.113425925925926E-2 | 5.6064814814814817E-2 | 4.0208333333333332E-2 | 2.0833333333333332E-2 | 1.7361111111111112E-2 | 5.1875000000000004E-2 | 3.125E-2 | 5.2847222222222219E-2 | 2.9305555555555557E-2
Forecasted | 0.022917 | 0.0090278 | 0.044444 | 0.032639 | 0.013889 | 0.013194 | 0.041667 | 0.03125 | 0.042361
line | 0 | 0.0625
Bus Run Time (min)

## Slide 16: U.S. BRT systems Actual run time performance
Chart: Preexisting Run Time
| 3.3333333333333333E-2 | 1.113425925925926E-2 | 5.6064814814814817E-2 | 4.0208333333333332E-2 | 2.0833333333333332E-2 | 1.7361111111111112E-2 | 5.1875000000000004E-2 | 3.125E-2 | 5.2847222222222219E-2 | 2.9305555555555557E-2
Forecasted | 0.022917 | 0.0090278 | 0.044444 | 0.032639 | 0.013889 | 0.013194 | 0.041667 | 0.03125 | 0.042361
line | 0 | 0.0625
Post Project | 0.025 | 0.010428 | 0.047627 | 0.032454 | 0.018056 | 0.0125 | 0.037292 | 0.025139 | 0.040625 | 0.019444
Bus Run Time (min)

## Slide 17: U.S. BRT systems Travel time reduction
Chart: 
Actual TT Reduction | 0.35 | 0.34 | 0.3 | 0.26 | 0.24 | 0.23 | 0.2 | 0.2 | 0.2 | 0.18 | 0.16 | 0.15 | 0.08
Forecasted TT Reduction | 0.19679 | 0.3125 | 0.19842 | 0.18826 | 0.051454 | 0.24 | 0.33333 | 0.20727 | 0.18919

## Slide 18: U.S. BRT systems Simplified run time estimation
Chart: U.S. BRT Systems
Preexisting | 80.7333 | 74.7 | 48 | 30 | 25 | 16.0333
Post Project | 68.5833 | 53.7 | 36 | 24 | 18 | 15.0167
Forecasted | 64 | 60 | 33 | 20 | 19 | 13
Quick Estimate | 70 | 34.6 | 32 | 19.5 | 23.5 | 14

## Slide 19: San Francisco BRT scenarios Simulated travel times
Chart: One-way Run Time (min.)
| A | B | C | D | E | F | G | H
Existing | 24.2 | 24.2 | 24.2 | 24.2 | 14.4 | 14.4 | 17.5 | 17.5
Baseline | 30.2 | 30.2 | 34.8 | 34.8 | 14.2 | 14.2 | 16.8 | 16.8
Simulation | 20.6 | 18.4 | 20.8 | 18.7 | 11.6 | 10.3 | 14.3 | 13.7

## Slide 20: San Francisco BRT scenarios Run time comparison
Chart: One-way Run Time (min.)
| A | B | C | D | E | F | G | H
Baseline | 30.2 | 30.2 | 34.8 | 34.8 | 14.2 | 14.2 | 16.8 | 16.8
Simulation | 20.6 | 18.4 | 20.8 | 18.7 | 11.6 | 10.3 | 14.3 | 13.7
Quick Estimation (High, Medium, Low) | 25.7 | 23.6 | 29.6 | 27.1 | 12.1 | 11.1 | 14.3 | 13.1
Quick Estimation (High, Medium, Low) | 18.9 | 17.3 | 20.85 | 19.05 | 10.6 | 7.7795 | 11.7 | 8.7795
Quick Estimation (High, Medium, Low) | 12.1 | 11 | 12.1 | 11 | 9.1 | 4.459 | 9.1 | 4.459

## Slide 21: What next? Do we change anything?
  For current projects
    Build some bus rapid transit
      Several SF Bay Area projects opening 2015-2020
    Document performance and assess forecasting success
  For future projects
    Seriously consider alternatives to simulation
    Try multiple methods and cross validate estimates

## Slide 22: The End Almost

## Slide 23: Words of wisdom Lessons from BRT implementers
  Understand your delay
    Every corridor is different
    Features, designs, treatments only effective if they address existing causes of delay
    (While not adding new sources of delay)
  Avoid overpromising in the face of uncertainty
    Lots of unknowns
    Regardless of forecasting, won’t know until buses on ground
  Specific TT savings not important if customer is happy
    In some cases, travel time savings failed to meet expectations,
    But ridership exceeded forecasts
    If the ride feels fast and customers are happy  success

## Slide 24: Words of wisdom Lessons from BRT implementers
  Need proof of concept
    Some cities started with less controversial corridor
    Many cities with BRT are working on new corridors
  Coalition building
    BRT meant to be cheaper and faster, but still challenging to implement
    Need coalition of support including community, politicians, businesses, etc.

## Slide 25: Thank you. Dan Tischler dan.tischler@sfcta.org