## Slide 1
Identifying Bicycle Trips in Routine Travel GPS Data:
Are Accelerometers Necessary?
May 18, 2015
TRB Applications Conference
Dara Seidl
Statistical GIS Analyst

## Slide 2: Introduction
GPS Travel Survey Considerations
Lower respondent burden and higher trip capture
GPS data processing challenges
Imputation of mode, trip purpose
Horizon of smartphone GPS, accelerometer
Experienced survey, opinion, policy research firm
Transportation, health, public policy, environment
In-house GIS department
Data collection & analysis in household travel research

## Slide 3: Central Questions
How can GPS trip characteristics be used to classify travel mode? (Part I)
What utility does accelerometer data provide in determining travel mode? (Part II)

## Slide 4: Background
Interest in Accelerometers
Measure physical activity
Uses in health travel research
Combine transportation and health data collection (NCHRP 2013)
Lower respondent burden
Mode identification in non-motorized travel (Oliviera et al. 2006)
Implementation Issues
Cost of additional device
Integration of data sets
If using smartphone:
  Background data logging
  Disruption of picking up phone
  Variations between phones and apps
User fatigue

## Slide 5: Accelerometer Data by Mode
Chart: Bike
| 15:47:15:57 | 15:47:15:243 | 15:47:15:506 | 15:47:15:671 | 15:47:15:865 | 15:47:16:125 | 15:47:16:286 | 15:47:16:521 | 15:47:16:635 | 15:47:16:822 | 15:47:17:23 | 15:47:17:261 | 15:47:17:473 | 15:47:17:653 | 15:47:17:842 | 15:47:18:34 | 15:47:18:303 | 15:47:18:420 | 15:47:18:620 | 15:47:18:820 | 15:47:19:26 | 15:47:19:219 | 15:47:19:419 | 15:47:19:619 | 15:47:19:839
 | -0.2 | 0.62 | 0.59 | 1.16 | -0.5 | -0.36 | 0.09 | -0.15 | 0.6 | -0.22 | -0.19 | 0.14 | 0.73 | 0.35 | -0.01 | 0.05 | -0.84 | -0.76 | -0.38 | 0.39 | 1.27 | 0.07 | 0.48 | 0.84 | 0.51
 | -0.53 | 2.11 | 0.35 | -1.25 | 0.62 | -0.11 | -0.14 | -0.95 | -0.24 | 0.02 | -0.9 | -0.16 | -0.47 | 0.34 | -0.19 | -0.19 | -0.13 | -0.43 | -0.25 | 0.19 | -0.75 | -0.12 | 0.94 | -0.22 | 0.19
 | -1.12 | -0.68 | 0.01 | -1.44 | -0.92 | -0.13 | 0.01 | -0.38 | -0.67 | -0.14 | -0.76 | -0.8 | -0.53 | -0.29 | -0.62 | -0.89 | -0.15 | -0.76 | -0.28 | -0.64 | -0.38 | -0.99 | -0.57 | -0.09 | -0.39
Chart: Bus
| 11:05:01:1 | 11:05:01:201 | 11:05:01:402 | 11:05:01:603 | 11:05:01:801 | 11:05:02:1 | 11:05:02:201 | 11:05:02:402 | 11:05:02:601 | 11:05:02:801 | 11:05:03:9 | 11:05:03:203 | 11:05:03:403 | 11:05:03:603 | 11:05:03:803 | 11:05:04:2 | 11:05:04:203 | 11:05:04:403 | 11:05:04:602 | 11:05:04:802 | 11:05:05:3 | 11:05:05:203 | 11:05:05:403 | 11:05:05:602
 | -0.05 | -0.05 | -0.03 | 0 | -0.01 | -0.01 | -0.03 | 0 | -0.01 | -0.01 | -0.01 | -0.02 | -0.01 | -0.02 | -0.04 | -0.01 | -0.04 | 0.01 | -0.02 | -0.02 | -0.01 | -0.01 | 0 | 0.02
 | -0.19 | -0.16 | -0.18 | -0.1 | -0.14 | -0.13 | -0.14 | -0.16 | -0.22 | -0.24 | -0.24 | -0.24 | -0.22 | -0.2 | -0.17 | -0.2 | -0.18 | -0.16 | -0.12 | -0.08 | -0.1 | -0.1 | -0.1 | -0.09
 | 0.97 | 0.91 | 0.87 | 0.93 | 0.98 | 0.92 | 0.93 | 0.99 | 0.9 | 0.88 | 0.85 | 0.92 | 0.91 | 0.92 | 0.92 | 0.94 | 0.91 | 0.9 | 0.91 | 0.93 | 0.91 | 0.96 | 0.95 | 0.94
Chart: Walk
| 11:13:33:12 | 11:13:33:214 | 11:13:33:422 | 11:13:33:624 | 11:13:33:823 | 11:13:34:24 | 11:13:34:222 | 11:13:34:424 | 11:13:34:623 | 11:13:34:826 | 11:13:35:22 | 11:13:35:222 | 11:13:35:424 | 11:13:35:622 | 11:13:35:822 | 11:13:36:22 | 11:13:36:224 | 11:13:36:422 | 11:13:36:741 | 11:13:36:822 | 11:13:37:78 | 11:13:37:246 | 11:13:37:656 | 11:13:37:659 | 11:13:37:823
 | -0.01 | -0.28 | 0.06 | 0.11 | 0.16 | 0.12 | -0.03 | -0.05 | 0.14 | 0.23 | 0.14 | 0.17 | -0.01 | -0.01 | -0.04 | 0.03 | 0.04 | 0.18 | -0.02 | 0.03 | -0.18 | -0.09 | 0.03 | 0.04 | -0.09
 | 0.65 | 0.64 | 0.53 | 0.86 | 0.58 | 0.62 | 0.93 | 0.74 | 0.58 | 1.04 | 0.67 | 0.73 | 0.97 | 0.75 | 0.78 | 0.85 | 0.51 | 0.75 | 0.79 | 0.51 | 0.4 | 0.23 | 0.46 | 0.69 | 0.52
 | 0.72 | 0.87 | 0.43 | 0.58 | 1.07 | 0.28 | 0.73 | 0.49 | 0.33 | 0.52 | 0.64 | 0.42 | 0.67 | 0.56 | 0.37 | 0.85 | 0.59 | 0.64 | 1.15 | 0.63 | 0.81 | 1.15 | 0.48 | 0.87 | 0.93
5-second samples captured by Android smartphone
X
Y
Z

## Slide 6: Survey Instruments
GPS Data Logger

## Slide 7: Methods Overview
Collect GPS and Diary Travel Data
Process Into Trips
Divide to 120-Second Segments
Identify Mode for Reference Segments
Random Forest Classification
Evaluate Mode Classification

## Slide 8: Data Characteristics
Participants
Number
6 Total
Geography
5 San Diego
1 Chicago
Age
Range: 24-30
Mean: 26
Trips
Number
92 trips
Duration
65 sec – 58 min
Length
0.1—12 miles
15.3/participant
Mean: 13 min
Mean: 2.6 miles

## Slide 9: Segment Characteristics
Following trip processing, confirmed trips divided into 120-second segments
543 segments
90 segments per participant
Chart: 120-Second Segments by Mode
| Auto | Bicycle | Bus | Metro | Walk
Cnt_MODE | 148 | 219 | 38 | 3 | 135

## Slide 10: Segment Variables
Maximum Speed
Mean Speed
Mean Heading Change
0-Speed Frequency
Seconds of Rest at Bus Stop
Chart: Maximum Speed (mph)

## Slide 11: Segment Variables
Chart: Mean Speed (mph)
Maximum Speed
Mean Speed
Mean Heading Change
0-Speed Frequency
Seconds of Rest at Bus Stop

## Slide 12: Segment Variables
Chart: Mean Speed (mph)
Maximum Speed
Mean Speed
Mean Heading Change
0-Speed Frequency
Seconds of Rest at Bus Stop

## Slide 13: Random Forest Classification
Machine learning algorithm
Grows many decision trees
Uses bagging to prevent overfitting
Reports most useful predictors
Success in travel mode classification (Stenneth et al. 2011; Ellis et al. 2014)

## Slide 14
Classification Results

## Slide 15: Segment Prediction Success
Actual Class | Total Class | Percent Correct | Auto N = 113 | Bicycle N = 189 | Bus N = 98 | Walk N = 140
Auto | 148.00 | 58.11% | 86.00 | 7.00 | 52.00 | 3.00
Bicycle | 219.00 | 80.82% | 14.00 | 177.00 | 23.00 | 5.00
Bus | 38.00 | 55.26% | 12.00 | 4.00 | 21.00 | 1.00
Walk | 135.00 | 97.04% | 1.00 | 1.00 | 2.00 | 131.00
Total: | 540.00 |  |  |  |  | 
Average: |  | 72.81% |  |  |  | 
Overall % Correct: |  | 76.85% |  |  |  | 

## Slide 16: Variable Importance
Chart: 
| Mean Speed | Max Speed | Zero Speed | Mean Head Change | Bus Stop
 | 100 | 59.6982 | 23.2674 | 8.1176 | 3.145

## Slide 17: Top Variables by Travel Mode
Chart: 
| Auto | Bicycle | Bus | Walk
Mean Speed | 100 | 100 | 71.0388 | 100
Max Speed | 70.5943 | 77.56 | 83.3987 | 24.3597
Mean Head Change | 58.6145 | 25.69 | 92.8619 | 8.8813
Zero Speed | 50.175 | 54.12 | 100 | 54.9802
Bus Stop | 46.4255 | 18.46 | 68.3299 | 5.5774

## Slide 18: Bigger Picture
Classification considers small 120s segments, rather than full trip characteristics
Considering micro- and macro-view of trips in tandem may produce better results
Even if segment is misclassified, multiple segments per trip can produce better estimates of overall trip modes
Bicycle
Bicycle
Bicycle
Auto
Bicycle
Bicycle
Bicycle
Trip 7

## Slide 19: Conclusions
Mode classification by 120 s captures typically under-represented multimodal trips (Clifton and Muhs 2011)
Overall 77% accuracy in segment mode prediction, 81% for bicycle
Random forest classification performs relatively better for non-motorized travel modes
Including accelerometer data as a classifying variable is Part II of this study…coming soon

## Slide 20
Questions?
Dara Seidl
Statistical GIS Analyst
d.seidl@srbi.com
Timothy Michalowski
Senior Statistical GIS Analyst
t.michalowski@srbi.com

## Slide 21: Letter to Participants