## Slide 1: Sample Expansion for Transit Rider Surveys
Experiments with Two Rail Systems

## Slide 2: Motivations
FTA requirements for rider surveys
  Model validation for major-project forecasting
  “Before” and “After” rider surveys for projects
Frequently asked questions:
  What is best practice for sample expansion?
  Are special on-to-off “surveys” worth the effort?

## Slide 3: Motivations (continued)
Sample expansion
  Computed weight for each survey record:
  actual trips in the cell
  Weight = ------------------------------------------------
  useable survey records in the cell
  Where the cell is an element of the sampling frame
    By route
    By route, direction, and time of day (TOD)
    By route, TOD, direction, and boarding stop
    By route, TOD, and on-to-off (or entry-to-exit) locations

## Slide 4: Experimental design
Find rider surveys for which station-to-station trip flows are known from fare-gate data
Compare accuracy of survey records expanded:
  To entry-station counts
  To entry-station to exit-station flows estimated through matrix filling with:
    Seed matrix = 1.0 for all cells
    Seed matrix = tabulated survey records
    Seed matrix = N% sample of fare-gate records

## Slide 5: Survey datasets
Washington DC Metrorail system (2008)
  58,100 records from 750,400 daily entries (7.7%)
  Paper survey forms with self enumeration
  After-the-fact tabulation of the data
Atlanta GA rail system (2009/2010)
  22,900 records from 195,500 daily entries (11.7%)
  Personal interviews with tablets
  Active sample monitoring and deficit repairs

## Slide 6: 1. Expansion to entry-station counts Estimated v. actual exits: Washington
AM
MD
PM
EV

## Slide 7: Expansion to entry-station counts (cont’d) Bias in estimated exits: Washington
Plotted points are the 86 rail stations
R Squared = 0.2064

## Slide 8: Bias in response rates: Washington
R Squared = 0.6139

## Slide 9: Expansion to entry-station counts (cont’d) Bias in estimated exits: Atlanta
R Squared = 0.022

## Slide 10: Bias in response rates: Atlanta
R Squared = 0.002

## Slide 11: Expansion to entry-station counts (cont’d) Estimated v. actual flows: Washington
AM
MD
PM
EV

## Slide 12: 2. Expansion to station-to-station flows
Cells in sample designed defined jointly by:
  Entry station and exit station by time period
  Expansion weight computed for records in each cell
  Number of actual trips divided by number of records
Method to estimate actual trips in each cell
  Matrix filling via iterative proportional fitting (IPF)
  Counts of station entries and exits  targets for rows and columns
  Seed matrix: Survey records? Sample of flows?

## Slide 13
Entry counts only
IPF: seed = 1’s
IPF: seed = survey records
IPF: seed = survey; 0.1 infills
IPF: seed = survey; 1.0 infills
IPF: seed = 20% flow sample
Method for Estimating Station-to-Station Flows
109%
39%
2. Expansion to station-to-station flows (cont’d) Percent RMSE by time period: Washington
Notes: Seed = 1 performs poorly for AM/PM peaks due to high directionality and clustering in the flows. The non-peak periods are much more evenly distributed, and therefore an evenly distributed seed does cause as many problems.

## Slide 14
39%
2. Expansion to station-to-station flows (cont’d) Percent RMSE by time period: Washington
Sampling Rate for the Sample of Entry-to-Exit Flows
20%
Notes: 100% sample would have all %RMSEs = 0

## Slide 15: 2. Expansion to station-to-station flows (cont’d) Sparseness of the flow table: Washington
Actual flows have relatively few empty cells
Low sampling rates lead to sparse seed matrices
Main effect is to empty out cells with 1-5 trips
  Actual: 28,466 trips
  5%: 0 trips
  20%: 20,101 trips
  50%: 24,127 trips
Percent of station-to-station cells with specified number of trips |  |  |  | 
Sample rate | 0 trips | 1-5 trips | 6-10 trips | >10 trips
100% | 8% | 38% | 15% | 39%
5% | 64% | 0% | 0% | 36%
10% | 51% | 0% | 10% | 39%
15% | 44% | 1% | 18% | 38%
20% | 38% | 13% | 11% | 38%
25% | 35% | 17% | 10% | 38%
30% | 32% | 17% | 13% | 38%
50% | 24% | 25% | 13% | 38%
80% | 18% | 33% | 12% | 38%

## Slide 16: 2. Expansion to station-to-station flows (cont’d) Comparison for AM flows: Washington
Records expanded with counts of station entries
Records expanded with flows developed from a 20% sample

## Slide 17: 2. Expansion to station-to-station flows (cont’d) Comparison for AM flows: Atlanta
Records expanded with counts of station entries
Records expanded with flows developed from a 20% sample

## Slide 18: Observations
Expansion to station-entry counts
  Errors in estimates of flows and station exits
  Income-related biases in response rates
    Evident with paper-based, post-processed survey
    Much less evident with combination of:
      Tablet-assisted personal interviews,
      Sample design based on fare-gate flows, and
      Real-time monitoring to ensure realization of the sample design

## Slide 19: Observations
Expansion to station-to-station flows
  Adds important information: station exits
  IPF application improves estimate flows significantly
    Seed matrix from survey records retains survey biases
    Seed matrix from independent sample of flows
      20-30% sample effective for these two systems
      Larger samples marginally better

## Slide 20: Implications for rider surveys
Method in the field matters
Second dimension helpful in all cases
Sample of flows helps
  With sample design and management
  With sample expansion
Extension to smaller-ridership cases
  Similar sample design, management, expansion
  Sparseness  grouping of stations/stops

## Slide 21: Thank you. Questions?