## Slide 1: Comparative Fidelity of Alternative Traffic Flow Models at the Corridor Level
A Case Study in Colorado Springs
15th Transportation Research Board
Transportation Planning Applications Conference
May 17 – 21, 2015 Atlantic City, New Jersey
Speed Data-ing Session: May 21, 2015
Thursday: 8:30 AM – 10:00 AM
Presented by:
Maureen Paz de Araujo, HDR
Carlos Paz de Araujo, University of Colorado
Kathie Haire, HDR

## Slide 2: Problem Statement
01
What is the problem the equation might solve?
How can we improve upon process and results?

## Slide 3: Problem Statement
Different simulation tools give different answers prompting the questions:
  Is there a “best” tool or a “right” answer?
  Is there a common thread among all tools and can it be improved upon?
  If so, can we improve upon the “answer” by tapping that common thread?
  How can we adapt to address emerging traffic flow modeling needs?
Fillmore St / I-25 DDI Build Alternative - MOE Results Comparison |  |  | 
Software/Intersection | Chestnut St | SB Ramps | NB Ramps
Synchro – on board | 27.6 sec/veh | 23.1 sec/veh | 23.1 sec/veh
Synchro - HCS | 22.8 sec/veh | 16.5 sec/veh | 22.9 sec/veh
VISSIM | 24.9 sec/veh | 18.1 sec/veh | 14.1 sec/veh
TSIS-CORSIM | 28.6 sec/veh | 23.9 sec/veh | 24.0 sec/veh
Fillmore Street/I-25 DDI Preferred Alternative – VISSIM MOEs
Intersection LOS/Delay Evaluation Fillmore/I-25 DDI – Colorado Springs, CO
LOS C
LOS B
LOS B
LOS D
LOS C
LOS C
LOS C
LOS C
LOS C
LOS C
LOS C
LOS C

## Slide 4: Emerging Trends in Traffic Flow Modeling
02
What emerging issues driving the search?

## Slide 5: Selecting the “Right” Tool can be Daunting - We see:
  Increasing Convergence: among macro, micro, and mesoscopic models
  Adaptations to Continuity Equation: to deal with real phenomena
  Addition of Multi-class Functionality: to expand reach of models
  Hybridization of Models: to combine advantages of macroscopic, mesoscopic and microsimulation models
Greenshield
LWR
Lighthill
Whitham
Richards
MACRO
MESO
MICRO
Convergence
Hybrid Models
Adaptations of Continuity Equation

## Slide 6: Traffic Flow Modeling Theoretical Foundations
03
What have we got to work with?
What do we know?

## Slide 7: The Fundamental Diagram is a Common Thread
Underpinning the models is the knowledge that there is a relation between the distance between vehicles and their travel speed
The Greenshields (1935) Fundamental Diagram expresses the relation using flow and density, where:
    Flow = q, average number of vehicles per unit length of road
    Density = ρ, average number of vehicles per unit of time
and:
    qcap = flow at capacity
    ρjam = jam density at which flow is zero
Schematic Fundamental Diagram
ρjam
ρ = Density
qcap = Flow at Capacity
q = Flow
qcap
Traffic Flow vs. Density
(Greenshields 1935 – Parabolic for Density – Flow )

## Slide 8: Role and Variations to the Fundamental Diagram
The Fundamental Diagram and Traffic Flow Equation provide a foundation for traffic flow modeling
Expression and shape of the fundamental relation has varied:
  Parabolic (Greenshields, 1935)
  Skewed Parabolic (Drake, 1967)
  Parabolic-linear (Smulders, 1990)
  Bi-linear (Daganzo, 1994)
Variables used to express the fundamental relation also vary:
  Density (ρ, rho) – Flow (q)
  Density (ρ, rho) – Velocity ()
Density – Flow Fundamental Diagram Plots
Density – Velocity Fundamental Diagram Plots
vmax
ρjam
vmax
ρjam
vmax
ρjam
Greenshields (parbolic) Daganzo (bi-linear) Smulders (parabolic-linear)
qcap
ρjam
qcap
ρjam
qcap
ρjam
Greenshields (parbolic) Daganzo (bi-linear) Smulders (parabolic-linear)

## Slide 9: From the Diagram came the Difficult Equation
    The Traffic Flow Equation is a non-linear partial differential equation:
        where:
        ρ (rho) = density (vehicles/unit of time)
        q = flow (vehicles/unit of distance)
        t = time
        = distance
        A closed-form solutions to nonlinear partial differential equations (PDE) are not easily attained.
Generic Type Traffic Flow Formulas:
  Drift (Free Flow) – First Order Model
q = ρv
where: q = flow
ρ = density (vehicles/unit of time)
v = velocity (unit of distance/unit of time)
  Diffusion (Random Velocities)
q = - D
where: D = the diffusion coefficient
  Complete/Combined – Second Order Model
q = ρv - D

## Slide 10: Traffic Flow Equation Solution
04
Can we solve the Traffic Flow Equation?
Then what can we do with the solution?

## Slide 11: Approaches to Solving the Traffic Flow Equation
Find special cases (solutions exist, are differentiable, or non-negative) with closed-form solutions, or solve the equation numerically (by approximation)
Estimate the solution using Method of Characteristics with x, t pairs; use diagraming because there is no closed-form solution.
Use a Self-Similar Solution approach - Convert the partial differential equation to an ordinary differential equation.
Schematic Diagram: Traffic Flow Dynamics for Congested Road Segment
Free traffic shown in blue; congested traffic shown in red.
Upstream and downstream boundary flows are time-dependent.
The jam forms at the intersection of the blue and red lines.
Credit: Lighthill–Whitham-Richards Model with Triangular Fundamental Diagram

## Slide 12
ρ = ρcrit (1 - ) q = ρ
where:
average =
0 , t0 = and t for the initial condition;
0 =0 and t0 =0 typical
From this solution we can solve for any of these variables as a function of the others:
  Freeflow speed (freeflow )
  Average speed (average )
  Capacity (Cap )
  Volume (Vol )
Closed-Form First Order Solution:

## Slide 13
q = ρ freeflow - ρ -
where:
ρ 2 dependence is parabolic
      ρ dependence is linear
thus:
ρ (x, t ) = ρcrit ( 1 + (
Closed-Form Second Order Solution:

## Slide 14: Next Steps
Determine how the traffic flow equation is implemented by various software
Apply closed-form/direct solutions to case study projects
Compare closed-form solution results to simulation solutions/results