## Slide 1: Taking a Walk:
Modeling Pedestrians and Bicycles at the Street Level
15th TRB National Transportation Planning Applications Conference
May 17-21
Atlantic City, NJ

## Slide 2: Where We’ve Been
Established practice that modeling and estimating active transportation demand requires a fine grained network and detailed zonal structure

## Slide 3: Case Studies
200 unit subdivisions in Southern New Castle County
  Suburban Middletown
    Case Studies 1 & 2
  Urban Middletown
    Case Studies 3 & 4

## Slide 4: Model Results for Study Area Trips
Chart: Daily Walking Trips within Study Area
| Peninsula Model | Micro Model | Parcel Model
Suburban Grid | 147 | 150.63 | 152.56
Suburban Cul-de-sac | 147 | 150 | 151
Urban Grid | 149.75 | 152 | 176
Urban Cul-de-sac | 149.25 | 150 | 162

## Slide 5: DelDOT Peninsula Model Background
Background:
  Delaware plus Maryland’s “Eastern Shore”
  Population of 1.2 Million
  5,375 sq. miles

## Slide 6: Developed LUTSAM to Streamline Process
Simulation
Travel Model
GIS
Community Design Scenarios
3-D Image Models
Peak Hour Travel
Auto, Bus, Bike, & Ped
Analysis & Visualization
Performance Measures

## Slide 7: Opportunities for Refinement
Enhanced network and zonal structure
Representation of biking and walking
Inclusion of accessibility

## Slide 8: Enhanced Network and Zonal Structure
Converted Model Network to Geodatabase
  Routable Centerline File
  RIMS Database
  GIS file that can be maintained annually
  Detailed information such as sidewalks, shoulder width, street width
Traffic Analysis Zone Resolutions
  Standard (973 Zones)
  Census Block (24,115 Census Blocks)
  Tax Parcel (403,791 Tax Parcels)
Resolution specified by TAZ

## Slide 9: Zonal Structure
PENINSULA
CENSUS BLOCK
TAX PARCEL

## Slide 10: Travel Network – New Castle County
PENINSULA
CENSUS BLOCK
TAX PARCEL

## Slide 11: Travel Network – Suburban Area
PENINSULA
CENSUS BLOCK
TAX PARCEL

## Slide 12: Destinations Available within 0.25 Miles
PENINSULA
1 INTRAZONAL
CENSUS BLOCK
57 CENSUS BLOCKS
TAX PARCEL
1257 PARCELS

## Slide 13: Representation of Biking and Walking
Annual Survey Background
  Delaware Travel Monitoring System (DTMS)
  Annual polling since 1997
  Survey conducted by University of Delaware’s Center for Applied Demography and Survey Research (CADSR)
  Computer Assisted Telephone Interviewing Over 60,000 survey trips in comprehensive database

## Slide 14: Representation of Biking and Walking
Enhanced DTMS survey in 2012
  Changes included introducing a new set of walking, bicycling, and transit specific questions
  Prompted respondent to report recreational trips
  Surveyed preference on comfort with walking or bicycling, maximum distance willing to use either mode

## Slide 15: Representation of Biking and Walking
Improved Results
  Number of reported walk and bike trips increased
Trip Mode | 2010 | 2011 | 2012* | 2013* | 2014*
Walk | 1% | 3% | 12% | 10% | 11%
Bike | 0% | 0% | 1% | 1% | 1%
Bus | 1% | 1% | 1% | 1% | 1%
Car | 98% | 95% | 86% | 89% | 86%
*enhanced DTMS survey year

## Slide 16: Improved Survey Results
Chart: Mode Share All trips
| 0.1 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 100 | 1000
CAR | 0.14719 | 0.24043 | 0.4934 | 0.7746 | 0.7379 | 0.90662 | 0.81787 | 0.96905 | 0.91553 | 0.97722 | 0.92412 | 0.96405 | 0.98725 | 0.98675 | 0.99465 | 0.97179 | 0.978 | 0.98712 | 0.97297 | 0.98529 | 1 | 0.96552 | 0.98551 | 0.94737 | 0.98758 | 0.77778
WALK | 0.82684 | 0.73723 | 0.48019 | 0.22063 | 0.24194 | 0.083192 | 0.16838 | 0.027079 | 0.077626 | 0.01519 | 0.056911 | 0.02451 | 0.007286 | 0.0022075 | 0.0026738 | 0.012539 | 0.013 | 0 | 0.009009 | 0 | 0 | 0.034483 | 0 | 0.052632 | 0.012422 | 0.22222

## Slide 17: Improved Survey Results
Chart: Mode share HBW
| 0.01 | 0.25 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 100 | 1000
CAR | 0 | 0 | 0 | 0.8254 | 0.97059 | 0.95833 | 0.97222 | 0.9759 | 1 | 0.97727 | 1 | 1 | 1 | 1 | 1 | 0.9899 | 0.99465 | 1 | 1 | 1 | 1 | 0.97143 | 1 | 1 | 1 | 0
WALK | 1 | 1 | 1 | 0.15873 | 0.029412 | 0.013889 | 0 | 0 | 0 | 0.022727 | 0 | 0 | 0 | 0 | 0 | 0.010101 | 0.0053476 | 0 | 0 | 0 | 0 | 0.028571 | 0 | 0 | 0 | 0

## Slide 18: Improved Survey Results
Chart: HBR TRIPS SHARE
| 0.1 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 100 | 1000
CAR | 0 | 0 | 0.061433 | 0.25397 | 0.22414 | 0.5 | 0.30851 | 0.80769 | 0.58929 | 0.94118 | 0.67308 | 0.75 | 0.9322 | 0.95122 | 0.96552 | 0.80556 | 0.90476 | 0.84211 | 0.8 | 0.88235 | 1 | 1 | 0.8 | 1 | 1 | 0.33333
WALK | 1 | 0.96795 | 0.89761 | 0.7381 | 0.73563 | 0.47368 | 0.64894 | 0.17308 | 0.375 | 0.029412 | 0.23077 | 0.125 | 0.016949 | 0.02439 | 0 | 0.083333 | 0.059524 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.66667

## Slide 19: Influence of Accessibility on Travel Mode
What level of accessibility influences travel mode the most?
  1 mile
  0.5 miles
  0.25 miles

## Slide 20: 1 Mile Accessibility (Walk Trips)
Chart: Avg Trips/Person by 1mi Accessibility (Walk, HBW+HBSHOP)
| 1 | 1 to 250 | 250 to 500 | 500 to 750 | 750 to 1000 | 1000 to 1250 | 1250 to 1500 | 1500 to other
 | 0 | 0.36364 | 0.64583 | 1.3 | 0.54545 | 0.75 | 2

## Slide 21: 0.5 Mile Accessibility (Walk Trips)
Chart: Avg Trips/Person by .50mi Accessibility (Walk, HBW+HBSHOP)
| 1 | 1 to 50 | 50 to 100 | 100 to 150 | 150 to 200 | 200 to 250 | 250 to 300 | 300 to other
 | 0.15385 | 0.32353 | 0.36957 | 0.73333 | 0.85 | 0.85714 | 0.5

## Slide 22: 0.25 Mile Accessibility (Walk Trips)
Chart: Avg Trips/Person by .25mi Accessibility (Walk, HBW+HBSHOP)
| 1 | 1 to 25 | 25 to 50 | 50 to 75 | 75 to 100 | 100 to 125 | 125 to 150 | 150 to other
 | 0.19608 | 0.48205 | 0.76471 | 0.8 | 1 | 1.4444 | 2

## Slide 23: 0.25 Mile Accessibility (Walk)
Chart: Trips/Person by Accessibility Walk, HBW+HBSHOP (.25 MI)
| 1 | 25 | 50 | 75 | 100 | 125 | 150
 | 0.19608 | 0.48205 | 0.76471 | 0.8 | 1 | 1.4444 | 2

## Slide 24: Next Steps
Develop hybrid model that includes accessibility, distance, and presence of infrastructure (Late Summer 2015)
Streamline inclusion in statewide model (Early Fall 2015)
Sensitivity testing (Late Fall 2015)

## Slide 25: Conclusions
Revised travel network, improved travel survey, and accessibility-based model will greatly enhance the ability to estimate active transportation at the street level
Revised process will streamline the ability to quickly provide results to decision makers

## Slide 26: Questions?
Scott Thompson-Graves
724-779-7940
sthompson-graves@wrallp.com
Mike DuRoss
302-760-2110
michael.duross@state.de.us
Li Li
703-293-7423
lli@wrallp.com
Dave Racca
302-831-1698
dracca@udel.edu
Ashley Tracy
724-779-7940
atracy@wrallp.com