## Slide 1: Outline
Prepared for TRB application conference 2015
Dynamic OD Demand Estimation based
on Observed Sensor Data
Jiangtao Liu, Arizona State University
Xuesong Zhou, Arizona State University

## Slide 2: Outline
Introduction to dynamic OD demand estimation
Methodology in our model
Numerical experiments
Existing challenges
Outline

## Slide 3: 1. Introduction
Dynamic OD demand: spatial and temporal trip distribution
  Static OD Demand
  Time-dependent profile
Traffic network: capacity, speed limit, jam density, backward wave speed
Observed flow and density data
Vehicle trajectory(Herrera et al. 2010)

## Slide 4: 1. Introduction
Dynamic Traffic Assignment

## Slide 5: 1. Introduction
Dynamic OD Demand Estimation

## Slide 6: 1. Introduction
Observed Traffic Data:
  Link Flow/Count: loop detectors
  Link Density: Video Image, or converted from speed data
  Speed Data (Link travel time): probe cars, detectors.
Automatic Vehicle Identification
Automatic Vehicle Location
Loop Detector
Video Image Processing
Point
Point-to-point
Semi-continuous
path trajectory
Continuous
path trajectory

## Slide 7: 1. Introduction
Link Flow/Count Data:
Link Speed Data: (1) estimate the traffic state; (2) easier to be observed than link density.

## Slide 8: 1. Introduction
One previous try to use probe speed data:
  (1) convert those speed data into dynamic link travel time
  (2) choose likely K-shortest paths
  (3) using route choice model
  (4) calculate link flow proportion
  : observed link count of link at time ;
  : estimated demand of OD pair at departure time

## Slide 9: 1. Introduction
One previous try to use probe speed data:
  Travel time of path 1 is equal to travel time of path 2
4
lanes
(
50
%)
1
lane
(
50
%)
4
lanes
(
80
%)
1
lane
(
20
%)
Path
2
Path
1
Path
2
Path
1
Without capacity constraints
With capacity constraints

## Slide 10: 2. Methodology in our model
Single-level path flow-based optimization model
Objective function:
  (1) minimize the deviation between estimated OD demand and historical OD demand;
  (2) minimize the deviation between estimated and observed traffic states (link flow/count, density, travel time)
Constraints:
  (1) Dynamic Network Loading of path flows based on Newell’s Kinematic Wave model (Newell, 1993)
  (2) Gap function-based dynamic user equilibrium conditions.
Algorithms: Lagrangian Relaxation

## Slide 11: 2. Methodology in our model
Partial derivatives(link flow, density, travel time) of path flow adjustment:
Link flow/count
Link density
Link travel time
The gradients of path flow:

## Slide 12: 2. Methodology in our model
Partial derivatives(link flow, density, travel time) of path flow adjustment:
  Individual link: free-flow, partially congested, fully congested;
  Two sequential links: queue spills back or not
(Ghali and Smith, 1995)

## Slide 13: 2. Methodology in our model
The calculation on link partial derivatives is still an approximation method.
Merging junction
Diverging junction

## Slide 14: 3. Numerical experiments
Illustration in a static case:
Link cost function:
Ta = FFTTa (1+ ra / capa)
Path | FFTT (min) | Capacity (veh/hr) | Assigned Flow (veh/hr) | Travel Time (min)
Path 1 | 20 | 3000 | 5400 | 56
Path 2 | 30 | 3000 | 2600 | 56

## Slide 15: 3. Numerical experiments
Illustration in a static case:

## Slide 16: 3. Numerical experiments
Illustration in a static case:

## Slide 17: 3. Numerical experiments
Network representation of a section of I-210 West bound corridor in LA

## Slide 18: 3. Numerical experiments
Observed & estimated lane volume on station a link
Observed & estimated speed on station c link

## Slide 19: 4. Challenges
Traffic network building: link capacity, speed limit, jam density, backward wave speed;
Historical dynamic OD demand: a good time-dependent profile for static OD demand
Observed data consistency: data quality control; cluster analysis
Travel behavior: dynamic user equilibrium, bounded rationality, road type preferences, and so on.
Algorithm: path partial derivative

## Slide 20
Thanks!